## Slide 1: Low Power System Design (PVL 207)

## Slide 2
Introduction
Device feature size
Voltage scaling Approaches
Challenges in Voltage Scaling Approaches
Architectural Level Approaches
Parallelism
Pipelining
Architectural level transformation
Supply Voltage Scaling for Low Power

## Slide 3: Introduction
Contribution of Various Sources of Power Dissipation
Pleakage = Vdd. Ileakage

## Slide 4: History of device size scaling for CMOS

## Slide 5: Different Approaches for Supply Voltage Scaling
Static Voltage Scaling: Different blocks or subsystems are given different fixed voltages.
Multilevel Voltage scaling (MVS): This is an extension of SVS where the supply voltage is switched between two or few fixed voltages.
Dynamic Voltage and Frequency Scaling (DVFS): This is an extension of MVS where a large number of voltage levels are dynamically applied for different workloads.
Adaptive Voltage Scaling (AVS): This is an extension of the DVFS where a control loop is used to adjust voltage and frequency for changing workload.

## Slide 6: Challenges of Supply Voltage Reduction
A factor of two reduction in supply voltage yields a factor of four decrease in energy.
Theoretical lower limit of supply voltage for CMOS circuit is 0.2V.
As supply voltage is lowered delay increases leading to dramatic reduction in performance.
Objective of voltage scaling is to scale Supply Voltage without compromise in performance.

## Slide 7: Challenges….
Power supply reduction helps digital circuits for power consumption but hurts analog voltage swing which should not be reduced.
Inherent transistor voltage gain decreases with reduced size technology, this implies larger number of stages to compensate the overall voltage gain.
Threshold voltages do not reduce linearly with size of technology, making the design with low VDD harder for analog circuits
Technology forecast

## Slide 8
a) Variation of normalized energy with respect to supply voltage
b) variation of delay with respect to supply voltage
Challenges in Supply Voltage Scaling

## Slide 9
Architectural Level Approaches for Voltage Scaling

## Slide 10: Parallelism
Parallel processing can be important technique for reducing power consumption in CMOS circuits.
Key approach is to trade area for power while maintaining the same throughput.
In simple terms, if the supply voltage is reduced by half, the power is reduced by one-fourth and performance is lowered by half.
The loss in performance can be compensated by parallel processing.

## Slide 11: Parallelism for Low Power
A 16 bit Adder
Architectural Level Approaches

## Slide 12
Parallel architecture of the 16-bit adder. MUX multiplexer

## Slide 14
Multi core for low power

## Slide 15
A four-core multiplier architecture
Multi-Core for Low Power

## Slide 16
Multi-core for Low Power
Important Issue : Increase in overhead, Limit on the supply
voltage, Increase in leakage current
This is the basis of the present day multi-core commercial processors
introduced by Intel, AMD and other Processor manufacturers
Thread level parallelism is explained in multi-core architectures to increase throughput of the processors.

## Slide 17
Pipelining for Low Power
Voltage scaling through optimal transistor sizing
Voltage scaling using high level transformation
Pipelining

## Slide 18: Basic Concept
What is pipelining?
It is an implementation technique where multiple tasks are performed in an overlapped manner.
Where can it be implemented?
It can be implemented where a task can be divided into two or more subtasks which can be performed independently.

## Slide 19: Pipeline Implementation
How it is implemented?
Different subtasks are performed by different hardware blocks known as stages.
The result produced by each stage is temporarily buffered in latches and then passed on to the next stage.

## Slide 21: Pipeline Performance parameters
Clock period
Frequency
Speedup: nk/k+(n-1)
Throughput: Number of tasks that can be completed per unit time.

## Slide 22: Pipelining for Low Power
Pipelined realization 16-bit adder

## Slide 24: Combining Parallelism with Pipelining
Parallel-pipelined realization of 16-bit adder. MUX multiplexer

## Slide 26
Optimal Transistor Sizing for Low Power

## Slide 27
Inversion Coefficient
IC
I0 = Technology current which is fixed for a particular technology
0.64 uA for nMOS and 0.135 uA for PMOS (0.18 um Technology)

## Slide 30: Multilevel Voltage Scaling
Clustered voltage scaling

## Slide 32: Dynamic Voltage and Frequency Scaling

## Slide 35: DVFS with Varying Work Load
Variable voltage processor μ( r)
Variable voltage generator V( r)
Variable frequency generator f( r)

## Slide 36: Variable Voltage Processor μ(r)
Frequency change in steps of 33 MHz
Voltage change in steps of 25 mV
Up to 200 frequency/voltage change per second

## Slide 39: Variable Voltage Generator V(r)

## Slide 40: References
Ajit Pal, “Low power VLSI Circuits and Systems” Springer, 2015.